## Slide 1: control your IoT device through phone
Made Adi Paramartha Putra
STMIK Primakara - 2020

## Slide 2: Today outline
Blynk as IoT Development
Introduction of Mobile Apps

## Slide 3: 1. Iot through mobile apps
Control your IoT device easily

## Slide 4
Internet of Things device able to controlled from anywhere and anytime even from a mobile phone application.

## Slide 5: how to control the device
End to end connection with device
Platform that used to control the device
Able to do something without worrying abotut the distance

## Slide 6: What is actual control
Monitoring
Is a method to simultaneously read the current condition of anything.
Operation
Is a method that able to simultaneously read the current condition as well as controling the device to do something new.

## Slide 7: An iot platform for business development
Blynk providing easy and fast access to controlling your IoT devices through your phone with many customizable control mode.

## Slide 8: BLYNK.Io
Providing free access to develop and control your first IoT Project

## Slide 9: Few THINGS that you need
Smartphone
• Android OS version 4.2+
• iOS version 9+
Blynk doesn't run on Windows Phones, Blackberries and other dead platforms. Sorry.
You can also run Blynk on emulators
IoT Device
Blynk can run on over 400 hardware modules. The most popular are:
• ESP8266
• ESP32
• NodeMCU
• Arduino (any model)
• Raspberry Pi (any model).
Internet Connection
To connect your hardware to the Internet, you can choose almost any module either built-in, or external shields
Supported connectivity
• WiFi
• Ethernet
• Cellular (GSM, 2g, 3g, 4g, LTE)

## Slide 10: how to start using blynk
Download Blynk in your Phone
Installing Blynk Library in Arduino IDE
Connect IoT device with auth token
Enjoy Blynking!

## Slide 11: download blynk app @mobile phone
Download Blynk in your Phone

## Slide 12: create an account
Create an account and sign in

## Slide 13: create an project
Create an project with gp1 as selected Pinout (ESP8266)

## Slide 14: Install blynk app @Arduino ide
Downloading Blynk Library from Website
Download Link:
After downloading, include the library (.zip) in Arduino IDE

## Slide 15: Install blynk app @Arduino ide - 2
Installing Blynk Library in Arduino IDE

## Slide 16: connect iot device w/ auth token
Connect IoT device with auth token
Token: ytK0zgzLGnmFHAjB4qq3mONctSlpTFvd

## Slide 17: connect iot device w/ auth token - 2
Choose the correct code for your board

## Slide 18: connect iot device w/ auth token - 3
Input the auth token into the code
Remember to input ssid information for internet connection

## Slide 19: connect iot device w/ auth token - 4

## Slide 20: connect iot device w/ auth token - 5

## Slide 21: the results (connection)

## Slide 22: the results - 2

## Slide 23: Enjoy the blynk app
Enjoy Blynking!

## Slide 24: How to show sensor value? For example dht22 sensor.

## Slide 25: Labeled value
Widget that used to shows sensor value

## Slide 26: How to do that ?
Add New Widget
Create two (2) widget to show current sensor value.
1 widget for temperature
1 widget for humidity
Settings up Widget
Modify the widget setting and make it able to receive the sensor value through Virtual Pin (Blynk)
Modify the Code
Add DHT22 Sensor Code into Arduino IDE to read the current sensor value, and send it with virtualWrite(virtualPin, value).
Mobile settings
Arduino settings

## Slide 27: How to do that ? - 2
Add New Widget
Settings up Widget
Modify the Code
Mobile settings
Arduino
settings

## Slide 28: the results - 3

## Slide 29: FOR THE PROJECT code
adiparamartha

## Slide 30: Task for you
Install Blynk app in your phone and Blynk Library in your Arduino IDE

## Slide 31: thanks!
Any questions?
@adiparamartha adi@primakara.ac.id

## Slide 32: Credits
Special thanks to all the people who made and released these awesome resources for free:
Presentation template by SlidesCarnival
Photographs by Unsplash